## Slide 1: Monitor Traffic Flow through In-band Network Telemetry (INT)
Chih-Yuan Sun (cs2368)
Yu-Hsuan Chen (yc2423)

## Slide 2: Outline
Goal
The Header Structure
Testing

## Slide 3: Goal
Understand how the packet is forwarded in the network.
What to monitor?
  The forwarding path
  The length of queue in each switch
  Time stayed in queue
  Ingress Timestamp
  Timestamp when the packet is first enqueued
Users can select the information that they want to know.

## Slide 4: Header Structure
INT Identifier <4 bytes>
  0 off / 1 on
INT Type <1 byte>
  destination based 0
  hop by hop 1
INT length <1 byte>
  Size of INT data
Byte 0 | Byte 1 | Byte 2 | Byte3
Ethernet |  |  | 
IPv4 |  |  | 
TCP |  |  | 
INT Identifier |  |  | 
INT Type | Rsvd | INT length | Rsvd
ins_cnt | max_hop_cnt | total_hop_cnt | Instruction map
INT INFO |  |  | 
Payload |  |  | 

## Slide 5: Header Structure
ins_cnt <1 byte>
  number of instruction
instruction map < 1 byte>
  e <1 bit>
  inst0 <1 bit>
    switch id
  inst1 <1 bit>
    time stayed in queue
  inst2 <1 bit>
    enqueued timestamp
    Length of queue
  inst3 <1 bit>
    Ingress timestamp
  rsvd <3 bits>
Byte 0 | Byte 1 | Byte 2 | Byte3
Ethernet |  |  | 
IPv4 |  |  | 
TCP |  |  | 
INT Identifier |  |  | 
INT Type | Rsvd | INT length | Rsvd
ins_cnt | max_hop_cnt | total_hop_cnt | instruction map
INT INFO |  |  | 
Payload |  |  | 

## Slide 6: Example
The information that the user want to know will be stored in the ‘INT INFO’ field.
Host 1
Switch 1
Switch 2
Switch 3
Host 2
ins_cnt | max_hop_cnt | total_hop_cnt | Instruction map
INT INFO |  |  | 
Payload |  |  | 
2 | 5 | 0 | 01100000
“Hello World” |  |  | 
2 | 5 | 1 | 01100000
(sw1) id = 1 |  |  | 
(sw1) t in q = 0x11 |  |  | 
“Hello World” |  |  | 
2 | 5 | 2 | 01100000
(sw2) id = 2 |  |  | 
(sw2) t in q = 0xd |  |  | 
(sw1) id = 1 |  |  | 
(sw1) t in q = 0x11 |  |  | 
“Hello World” |  |  | 
2 | 5 | 3 | 01100000
(sw3) id = 3 |  |  | 
(sw3) t in q = 0x7 |  |  | 
(sw2) id = 2 |  |  | 
(sw2) t in q = 0xd |  |  | 
(sw1) id = 1 |  |  | 
(sw1) t in q = 0x11 |  |  | 
“Hello World” |  |  | 
2 | 5 | 3 | 01100000
(sw3) id = 3 |  |  | 
(sw3) t in q = 0x7 |  |  | 
(sw2) id = 2 |  |  | 
(sw2) t in q = 0xd |  |  | 
(sw1) id = 1 |  |  | 
(sw1) t in q = 0x11 |  |  | 
“Hello World” |  |  | 

## Slide 7: Test Result